## Slide 1: Introduction to Verilog HDL

## Slide 2
Created By:
Behnam Akbari
bAkbari@ee.sharif.edu
www.verilog.blog.ir

## Slide 3
Sources: - Verilog HDL, Samir Palnitkar - MuhammadUzair Rasheed Slides - Online material, Chris Fletcher, UC Berkeley - A Crash Course in Verilog, Pantech Solutions

## Slide 4: Why we study Verilog!
You’re going to have one Verilog question in midterm exam and one in final exam (each constituting 2-3 points).
Your homework assignments usually have a Verilog coding question.
You are going to write Verilog codes for laboratory experiments number 4,8,9,10 and implement on CPLD.
Verilog is an important HDL, which you will most likely need, especially if you choose Digital Systems as your major field.

## Slide 5: What is HDL?
Hardware description language describes the hardware of digital systems in textual form.
Unlike software programming languages, HDLs model the structure of hardware performing concurrent execution of statements.
HDLs are used to simulate designs before fabrication.
HDLs can verify the functionality VLSI with millions of gates.
Virtually every chip (FPGA, ASIC, CPLD, ...) is designed using either Verilog or VHDL.

## Slide 6: Most Commonly used HDLs
Verilog
  Verilog HDL is commonly used in the US industry. Major digital design companies use Verilog HDL as their primary choice.
  Most commonly used in the design, verification, and implementation of digital logic chips
  Verilog uses a C-like syntax.
VHDL (VHSIC (Very High Speed Integrated Circuits) hardware description language)
  VHDL is more popular in Europe.
  commonly used as a design-entry language for field-programmable gate arrays. Field-Programmable Gate Array is a type of logic chip that can be programmed.

## Slide 7: Verilog Simulator
  There are many logic simulators used for Verilog HDL. Most common are:
  Xilinx
  Veriwell
  ModelSim
  Quartus
  Quartus and ModelSim are widely used.

## Slide 8: Getting started…
A Verilog program for a particular application consists of two blocks
Design Block (Module)
Testing Block (Stimulus)

## Slide 9: Design Block
Design Methodologies:
Two types of design methodologies
Top Down Design
Bottom Up Design
Design Block
inputs
outputs

## Slide 10: Top Down Design
In Top Down design methodology, we define the top level block and identify the sub-blocks necessary to build the top level block. We further divide the sub-block until we come to the leaf cells, which are the cells which cannot be divided.

## Slide 11: Bottom Up Design
In a Bottom Up design methodology, we first identify the building blocks , we build bigger blocks using these building blocks. These cells are then used for high level block until we build the top level block in the design

## Slide 12: Module Representation
Verilog provides the concept of module
A module is a
Basic building block in Verilog
It can be a single element or a collection of lower design blocks
A verilog code starts with module
Syntax:
module <module-name>(inputs, outputs) ;
// Declare inputs and outputs
  …………
…………
…………
endmodule
Don’t forget the semicolon!

## Slide 13: Input/Output Declaration
Once the module is defined, the inputs and outputs are to be declared explicitly. e.g.
input a , b ; // 2 single-bit inputs
If input or output is more than 1 bit, the definition will be:
input [3:0] A, B; // 4-bit inputs A3-A0 and B3-B0
output [1:4] C; // 4-bit output C1-C4

## Slide 14: Setting Value to Variables
assign X=<size>’<base><value>
where
  <size> is the number of bits. If left out, the default value of 32 bits is used
  <base> is b, o, d, or h for binary, octal, decimal, or hexadecimal. If left out, the default is decimal
  <value> is any legal number for the specified base. A ‘z’ or a ‘?’ instead of a digit represents a high impedance signal in an integer. An ‘x’ instead of a digit in an integer represents an undefined signal.
  For negative numbers use a minus sign(-) before <size>.

## Slide 15
Examples:
171 - size = 32, base = 10
’h2f3 - size = 32, base = 16
12’b1111_0000_1011 - size = 12, base = 2
Underscore(_) is used only to improve readability.
-3’b11? - size = 3, base = 2
a negative binary number whose LSB is unknown
16’O101342 - size = 16, base = 8
8’hZ - size = 8, base = 16
a hexadecimal number whose bits are of high impedance
Setting Value to Variables