## Slide 1: Levels of Abstraction

## Slide 2: Levels of Abstraction
Behavioral
(Procedural Modeling)
Module’s high-level algorithm is implemented with little concern for the actual hardware
Gate-Level
Data Flow
(Continuous Assignment)
Module is implemented by specifying how data flows between registers.
(Structural Modeling)
Module is implemented in terms of concrete logic gates and their interconnections.

## Slide 3: Data Flow Modeling
Most common operators:

## Slide 4: Data Flow Modeling
assign x = 3’b010 + 3’b100; // x=3’b110
assign x = 3’b010 && 3’b100; // x=(0+1+0)&(1+0+0)=1’b1
assign x = 3’b010 & 3’b100; // x=3’b000
assign x = !(3'b101) // x=~(1+0+1)=1’b0
assign x= ~(3'b101) // x=3’b010
assign x = 3’b111>> 2; // x=3’b001
assign x = 3’b111<< 2; // x=3’b100
assign y = x >> 2; // shift x to right by 2 bits

## Slide 5
9. assign a= |(3’b101); // a=1|0|1=1: Reduction OR
assign a={2{3’b110}}; // replication: a=6’b110110;
11. assign {cout , sum} = a + b + cin; // concatenation
  assign b = 3’b101, c =3’b 111;
  assign a = {b, c} // a = 101111
12. assign y = s ? b : a // 2×1 MUX
if s = 1 then y=b otherwise y = a
Data Flow Modeling

## Slide 6
13. assign y = s1 ? ( s0 ? d : c ) : ( s0 ? b : a ); // 4×1 MUX
Data Flow Modeling

## Slide 7: Gate-Level Modeling
In gate level modeling a circuit can be defined by use of primitive logic gates.
These gates are predefined in Verilog library.
The basic gates and their syntax is as follows:
and(output, inputs);
or(output, inputs);
not(outputs, input);
buf(outputs, input);
xor(output, inputs);
nor(output, inputs);
nand(output, inputs);
xnor(output, inputs);

## Slide 8: Gate-Level Modeling
In order to label each gate the following syntax can be used:
not my_gate(aBar, a);

## Slide 9: Gate-Level Modeling (Tristate Buffers)
bufif1 gate1(out, in, en);
bufif1 gate2(out, in, en);

## Slide 10: Gate-Level Modeling (Tristate Buffers)
NMOS conducts when its gate voltage is ‘1’ and PMOS conducts when its gate voltage is ‘0’. So the MOSFETS can be modeled as switches. In this table ‘0’ for MOSFETs implies an open switch, whereas ‘1’ implies a closed switch.

## Slide 11: Module Instantiation
Module instantiation is a process of connecting one module to another. A similar process in C language is calling a function.
For example in a test bench or stimulus the top level design has to be instantiated

## Slide 12: Testing Block (Stimulus)
In order to test your circuit a test bench code is to be written which is commonly called Stimulus.
The design block has to be instantiated.
It displays the output of the design based on the inputs.

## Slide 13: Example
2- Input AND Gate
The Design and Stimulus blocks will be as follows:

## Slide 14: Design Block
    module practice (y, a, b); // module definition
    input a, b; // by default it takes 1 bit input
    output y; // single-bit wire output
    and gate_1(y, a, b);
    endmodule
1) Gate-Level Modeling

## Slide 15: Design Block
2) Data Flow Modeling
    module practice (y, a, b); // module definition
    input a, b; // by default it takes 1 bit input
    output y; // single-bit wire output
assign y = a & b; // continuous assignment
    endmodule

## Slide 16: Stimulus Block (Optional)
module stimulus;
reg a, b;
wire y;
//Instantiate the practice module
practice p0(y, a, b);
initial
begin
a=0; b=0;
#5 a=1; b=1;
#5 a=0; b=1;
#5 a=1; b=0;
#5 a=1; b=1;
#5 $stop; // stop the simulation
#5 $finish; // terminate the simulation
end
initial
begin
$display("|%b| and |%b| = ", a, b);
$monitor ($time, "|%b |" , y);
end
//initial
//$vw_dumpvars; // display the simulation in the form of timing diagram
endmodule