## Slide 1: Modeling Combinational Circuits Hierarchical Design

## Slide 2: 1-bit Ripple Carry Full Adder

## Slide 3: 1-bit Ripple Carry Full Adder (Gate-Level Modeling)
module OneBitFA (sum, c_out, a, b, c_in);
output sum, c_out;
input a, b, c_in; // I/O Port declaration
wire s1, c1, c2; // Internal nets
xor (s1,a,b);
and (c1,a,b);
xor (sum,s1,c_in);
and (c2,s1,c_in);
or (c_out,c2,c1);
endmodule

## Slide 4: Instantiation & Connecting Ports
Connecting ports by ordered list
The signals to be connected must appear in the module instantiation in the same order as the ports in the port list in the module definition.
e.g. > OneBitFA fa0(sum, c_out, A, B, c_in);
Connecting ports by name
For large designs where modules have 50 ports remembering the order of ports is error prone. So connection by name comes in handy.
e.g. > OneBitFA fa1(.c_out(c1), .c_in(c0), .sum(Sum), .a(A), .b(B));
Unconnected ports
Verilog allows ports to remain unconnected. You might not be interested in connecting some port to external signals.
e.g. > OneBitFA fa2(sum, , A, B, c_in)
e.g. > OneBitFA fa3(.c_in(c0), .sum(Sum), .a(A), .b(B));
// In both examples output port c_out is unconnected.

## Slide 5: Module Ports

## Slide 6: Example 4-bit Ripple Carry Adder
1-bit FA
1-bit FA
1-bit FA
cin
a0
b0
s0
c1
1-bit FA
a1
b1
s1
c2
a2
b2
s2
c3
a3
b3
s3
cout

## Slide 7
4-bit Ripple Carry Adder
XOR, AND, OR Gates
1-bit FA #4
XOR, AND, OR Gates
1-bit FA #3
XOR, AND, OR Gates
1-bit FA #2
XOR, AND, OR Gates
1-bit FA #1

## Slide 8: Top Level Module (4-bit FA)
module FourBitFA(sum,c_out,a,b,c_in);
output [3:0] sum;
output c_out;
input [3:0] a, b;
input c_in; // I/O port declaration
wire c1,c2,c3; // internal nets
OneBitFA fa0(sum[0],c1,a[0],b[0],c_in);
OneBitFA fa1(sum[1],c2,a[1],b[1],c1);
OneBitFA fa2(sum[2],c3,a[2],b[2],c2);
OneBitFA fa3(sum[3],c_out,a[3],b[3],c3);
// Instantiate four 1-bit full adders
endmodule

## Slide 9: Test Bench (stimulus) (Optional)
// define stimulus top-level module
module stimulus;
reg [3:0] a,b; // set up variables
reg c_in;
wire [3:0] sum;
wire c_out;
/* Instantiate the top-level module FourBitFA and call it my_FA */
FourBitFA my_FA(sum,c_out,a,b,c_in);

## Slide 10
// stimulate inputs
initial
begin
a = 4'b0000; b = 4'b0010; c_in = 1'b0;
#1 $display (“ a = %b, b = %b, c_in = %b, sum = %b", a, b, c_in, sum);
a = 4'd1; b = 4'd2; c_in = 1'b1;
#2$display (“ a = %b, b = %b, c_in = %b, sum = %b", a, b, c_in, sum);
a = 4'hf; b = 4'ha; c_in = 1'b0;
#2$display (“ a = %b, b = %b, c_in = %b, sum = %b", a, b, c_in, sum);
end
endmodule

## Slide 11: 4-bit Adder/Subtracter

## Slide 12: 4-bit Adder/Subtracter (Gate-Level Modeling)
module AddSub(a, b, Cin_Bin, sub, result, Cout_Bout);
input [3:0] a, b;
input Cin_Bin, sub;
output [3:0] result;
output Cout_Bout;
wire B, CI, CO;
xor x1(B, b, sub); // Bitwise XOR
xor x2(CI, Cin_Bin, sub);
FourBitFA adder(result, CO, a, B, CI);
xor x3(Cout_Bout, CO, sub);
endmodule