## Slide 1: Modeling Sequential Circuits always Block Assignments

## Slide 2: always Block in Sequential Logic
always@(posedge Clock)
always at the positive edge of the clock
always@(negedge Clock)
always at the negative edge of the clock

## Slide 3: Blocking and Non-blocking Assignments
Blocking assignments
  block the remaining code from executing until a delay has passed
  Non-blocking assignments
  set up the output to change at a future time, and continue executing the next statements

## Slide 4: Blocking and Non-blocking Assignments
Blocking Assignments
  ff1 = #3 ff2; // ff1 changes at time 3
  ff2 = #3 ~ff1; // ff2 changes at time 6
Non-blocking Assignments
  ff1 <= #3 ff2;
  ff2 <= #3 ~ff1;
  // Both flip-flops change simultaneously at time 3

## Slide 5: Blocking and Non-blocking Assignments
Blocking Assignments
  count = count + 1;
  count = count + 2;
  // The result is: count = count + 3
Non-blocking Assignments
  count <= count + 1;
  count <= count + 2;
  // The second statement overrides the first, so: count = count + 2

## Slide 6: Non-Blocking Assignment
always @ ( posedge Clock ) begin
  B <= A ;
  C <= B ; // C is set the value of B just before the clock edge
  D <= C ;
end

## Slide 7
always @ ( posedge Clock ) begin
  B = A ;
  C = B; // C is set the value of B just after the clock edge i.e. A
  D = C ;
end
Blocking Assignment